## Slide 1
Corentin Damman
October 30, 2020
FPGA Contest 2020
Shared House Live Sensors
Notes: Choose from the existing cover option or create your own replacing the visual from the Photo library on Brand Connect

## Slide 2: Agenda
Abstract
Idea
Concept
Realization
Status
Project outlook
Project name

## Slide 3: Arrow FPGA Contest 2020
  The „Shared House Live Sensors“ project allows to share multiple sensors data live on a website
  It enables my roommates to see live data from our living room
  Features:
    Updates every minute, data kept in a database for the last 7 days
    Live data available on this website: https://pi.cdamman.eu/livesensors
    5 different sensors
      Temperature with AnalogMax sensor
      Temperature & Humidity with DHT11 sensor
      Smoke sensor with AnalogMax sensor
      Accelerometer with AnalogMax sensor
Summary

## Slide 4: Arrow FPGA Contest 2020
IdEa
My roommates complain all the time that
  It is too cold in their room
  It is too hot in the living room
  There are toast burnt in the toaster
  etc …
All these are very subjective feelings
What if I could give them objective data to prove they‘re wrong?

## Slide 5: Arrow FPGA Contest 2020
Concept
How to do that?
What we need
  A board with a lot of sensors, including (at least) temperature (“It’s too cold/too hot here” issue) and smoke detector (“burnt toast” issue)
  An online website
  A connection between the board and the website

## Slide 6: Arrow FPGA Contest 2020
Realization
The AnalogMax board is the perfect fit for this!
  Embeds a lot of sensors
  Enables to add more sensors with GPIOs and ADCs
  I already added one DHT11 sensor (1-Wire protocol implemented in VHDL)
  An embedded NIOS processor is used to gather all data from sensors and communicate with the serial USB link
For the website:
  I used a Raspberry Pi to host the server
  The AnalogMax board is connected using serial USB link
  A Python script is called every minute to acquire data and update plots

## Slide 7: Arrow FPGA Contest 2020
Status
Live sensors are now available online for my roommates…
… but also the rest of the world!
  Website link: https://pi.cdamman.eu/livesensors
  Github repository: https://github.com/cdamman/SharedHouseLiveSensors
RaspBerry Pi with serial USB
AnalogMax board
DHT11 sensor

## Slide 8: Arrow FPGA Contest 2020
Status: temperature sensors
My roommate turned on the heating
During the night, it’s colder!
All cooking in the living room

## Slide 9: Arrow FPGA Contest 2020
Status: temperature sensors
Cooking + window opened during autumn

## Slide 10: Arrow FPGA Contest 2020
Status: temperature sensors
Who burnt a toast??!

## Slide 11: Arrow FPGA Contest 2020
Status: temperature sensors
Who moved my board??!

## Slide 12: Arrow FPGA Contest 2020
Project outlook
Next steps and future plans:
  Add more sensors
    Motion sensor: is there someone in the living room?
  Add “is the heating on?” indicator on the website
    If living temperature > temperature programmed in the thermostat -> the heating is on
  …